Ultra SCSI CardBus PC Card for PowerBook
CB31Pismo

CB31PB is renewed as CB31Pismo !

Add Ultra-SCSI port to your
  PowerBookG3 (Wallstreet 1988, Lombard 1999), 
  PowerBook500/400 (Pismo, 2000) and 
  PowerBookG4 (Titanium).

Get DeskTop performance and Ultra-SCSI speed up to 
20MB/Sec.

Supports Ultra-SCSI device and legacy SCSI device.
HardDisk, CD-R/W, Scanner, FilmScanner, ORB, Jaz, and MO.

Includes SCSI-2 Hi-Density 50P cable and HD50-C50 Adapter.

Includes Disk formatter and Auto Mounter utility.

Includes SCSI configuration Utility.

Supports softRAID (softRAID,LLC.)

Q. What is difference from CB31PB (Our former product)?

A. The only difference is bundled cable.

| CB31PB | Hi-density 50pin cable Centronics 50pin cable |
| --- | --- |
| CB31Pismo | Hi-density 50pin cable Hi-Density 50F to Centronics 50M adapter |  |

# Features

Supports Ultra SCSI rates up to 20MB/sec.

32bit databus and 33MHz operation.

Supports bus mastering data transfer.

Ready for PowerManagement.

Low power consumption.

Supports scatter/gather and tagged queue.

# System Requirements

PowerBook G3/G4 with CardBus ready PC Card Slot.

PowerBookG4 (Titanium)

PowerBook 500, 400 (2000 Pismo)

PowerBookG3/400, G3/333 (1999 Lombard)

PowerBookG3/300, G3/292, G3/266, G3/250, G3/233 (1998,Wallstreet)

MacOS 8.6 / 9 / 9.0.2 / 9.0.4 / 9.1 / 9.2.x / X v10.1.x

# Device List

| [CD-R/W Drives] | TEAC | CD-R56S, CD-R824S |
| --- | --- | --- |
|  | JVC | XR-S4224M |
|  | Plextor | PX-412Ce, PX-R820 |
|  | YAMAHA | CDR400tk, CRW6416SX, CRW8424SX, CRW4416SX |
|  | HP | CD-writer 9600se |
|  | HP. Ricoh. Plextor. other Ultra-SCSI or SCSI CD-R/W drives. |
| [Film Scanner] | Nikon | Coolscan III, Super CoolScan 2000, CoolScanIII LS-30 |
|  | Minolta | DimageScanMulti F-300 |
|  | Canon | FS2710 |
|  | Poraroid | SprintScan 4000 |
|  | EPSON |  |
| [Image Scanner] | EPSON | Perfection 1200S, Expression 800, Expression 1600, GT-9600, GT-7000S, GT-7600S, GT-2200, ES-2000, ES-6000H |
|  | Canon | CanoScan FB620S |
|  | Microtec | ScanMakerX6 |
|  | UMAX | Mirage II,Mirage II Se,PowerLook 3000 |
|  | Agfa | Arcus II, Duoscan HiD |
|  | HP |  |
| [MO Drive] | Olympus | 640MO TURBO, 640MO TURBO LE, 640S II |
|  | Fujitsu | SMB-640D2 |
|  | Mitsubishi | MK640KF, MK640KC, MK640LG |
| [Other Removable Media] | iomega | JazV2000S, Zip250 |
|  | Castlewood | ORB 2.2GB |
| [PC Card Drive] | SCM | PCD600 |
| [Hard Disk drives] |  |  |
| * Learn updated information at www.ratocsystems.com/english/ |

# Specifications

| Data transfer rate | Up to 20MB/sec with Ultra SCSI devices Up to 10MB/sec with Fast SCSI devices |
| --- | --- |
| Termination type | Internal active termination provided |
| Operating requirements | CardBus PC Card slot Power Requirement +3.3V 130mA(idle), 300mA(MAX), 77mA(Power save mode) Temperature from 0(C to 55(C Relative humidity 20 to 80% (Non-condensing) |
| Package includes | CB31 Ultra SCSI CardBus PC Card Ultra SCSI cable with a Hi-Density 50pin connector(2feet) Hi-Density 50F to Centronics 50M adapter Software CD-ROM CB31 driver SCSI Configuration utility B's Crew Lite 3.1.1e CD-ROM User's manual Software License Agreement |
| Physical characteristics | 54.0mm(W) x 85.6mm(L) x 5.0mm(H) (PC Card Standard Type II) |